## Slide 1: FTOT Hazard Resilience Assessment
Ji Yun Lee
Assistant Professor
Department of Civil and Environmental Engineering, Washington State University
Jie Zhao
Ph.D. Student
Department of Civil and Environmental Engineering, Washington State University
Aug 17th , 2021

## Slide 2
Procedure of SCR Assessment
Framework for quantifying the effect of hazard event on SCR:
Risk assessment and recovery estimation
2.Newly developed Python file
Resilience assessment
3.Modified FTOT
HAZUS-MH
1.Scenario hazard analysis
FTOT resilience assessment package:

## Slide 3
2. Newly Developed Python File
Damage state probabilities of bridges and facilities
Time-varying capacity of facility and edge
Newly developed Python file:
Assess facility/edge capacity
Estimate their recovery processes
Earthquake
Facility capacity

## Slide 4
3. Modified FTOT Files
Modifications to FTOT:
o1 step
o2 step
for each time step：
s step
f step
c step
g step
p step
d step
m step
Overall steps
ftot_pulp_weely.py
Resilience calculation
ftot.py
ftot.py:
Incorporate the iteration structure
Add resilience calculation process
ftot_pulp_weekly.py:
Change facility/edge capacity
Change the objective function in o2 step:
Total costs =
Transportation costs
Un-met demand penalty
Processor construction costs
Operation costs
Repair costs
“capacity” in facility table in o1 step
“capacity” at “max route capacity” constraint in o2 step

## Slide 5
Resilience Calculation
Resilience:
Earthquake
Performance indicator
Performance indicators:
Unmet-demand ratio (Beheshtian et al., 2019)
Fulfillment rate of supplier (Barroso et al., 2015)
Cost-efficiency (Vugrin et al., 2011)
Reference
Beheshtian, A., Donaghy, K. P., Geddes, R. R., & Rouhani, O. M. (2017). Planning resilient motor-fuel supply chain. International Journal of Disaster Risk Reduction,24, 312-325. doi:10.1016/j.ijdrr.2017.06.021
Barroso, A. P., Machado, V. H., Carvalho, H., & Cruz Machado, V. (2015). Quantifying the supply chain resilience. Applications of Contemporary Management Approaches in Supply Chains. https://doi.org/10.5772/59580
Vugrin, E. D., Warren, D. E., & Ehlen, M. A. (2011). A resilience assessment framework for infrastructure and economic systems: Quantitative and qualitative resilience analysis of petrochemical supply chains to a hurricane. Process Safety Progress,30(3), 280-290. doi:10.1002/prs.10437

## Slide 6: Thank You
Image sources: https://pixabay.com/en/question-question-mark-help-2309042/